## Slide 1: Programmable Logic Devices

## Slide 2: Definitions
Programmable Logic Device (PLD):
  Also known as “Field Programmable Logic Device (FPLD)”
  An integrated circuit chip that can be configured by the user to implement different digital hardware.

## Slide 3: Programmable Logic Devices
PLD (generic)
  An IC where the logic function can be programmed into it after manufacture
  In some cases, it can be reprogrammed if a bug in the design is discovered
PLA (programmable logic array)
  The first PLD on the market
  Two level AND/OR array structure with user programmable connections
PAL (programmable array logic)
  Appeared on the scene after PLA’s
  Lower cost
  The MSI of the programmable industry; sometimes simply called PLD
ROM (read-only memory)
  Originally not thought of as a programmable device at all – simply a memory for holding machine specific information, such as the control store operation
CPLD (complex programmable logic device)
  A collection of PLD’s on a chip with programmable on-chip interconnections
FPGA (field programmable gate array)
  Another scheme developed same time as CPLD
  Large number of basic logic blocks (simple gates) with prog X/Y interconnection

## Slide 4
The first three varieties(ROM, PLA, PAL) are quite
similar to each other:
  - They all have an input connection matrix, which connects the inputs of the device to an array of AND-gates.
  - They all have an output connection matrix, which connect the outputs of the AND-gates to the inputs of OR-gates which drive the outputs of the device.

## Slide 5: PLD
The differences between the first three categories are these:
  1. In a ROM, the input connection matrix is hardwired. The user can modify the output connection matrix.
  In a PAL/GAL the output connection matrix is hardwired. The user can modify the input connection matrix.
  In a PLA the user can modify both the input connection matrix and the output connection matrix.

## Slide 6: Purpose of PLDs
Permits elaborate digital logic designs to be implemented by the user on a single device.
Is capable of being erased and reprogrammed with a new design.

## Slide 7: Advantages of PLDs
Programmability
Re-programmability
  PLDs can be reprogrammed without being removed from the circuit board.
Low cost of design
Immediate hardware implementation

## Slide 8: Types of PLDs
PLD
SPLD
PAL
GAL
HCPLD
CPLD
ROM
PLA
FPGA

## Slide 9: Types of PLDs
SPLDs (Simple Programmable Logic Devices)
  ROM (Read-Only Memory)
  PLA (Programmable Logic Array)
  PAL (Programmable Array Logic)
  GAL (Generic Array Logic)
HCPLD (High Capacity Programmable Logic Device)
  CPLD (Complex Programmable Logic Device)
  FPGA (Field-Programmable Gate Array)

## Slide 10: SPLDs
In ROM, the input connection matrix is hardwired and the user can only modify the output connection matrix.
In PAL and GAL the output connection matrix is also hardwired and the user can modify the input connection matrix.
In PLA the user can modify both the input connection matrix and the output connection matrix.

## Slide 11: HCPLDs
CPLD (Complex Programmable Logic Device)
  Lies between PALs and FPGAs in degree of complexity.
  Inexpensive
FPGA (Field-Programmable Gate Array)
  Truly parallel design and operation
  Fast turnaround design
  Array of logic cells surrounded by programmable I/O blocks

## Slide 12: General structure of PLDs.

## Slide 13: Programmable Logic Organization
Pre-fabricated building block of many AND/OR gates (or NOR, NAND)
"Personalized" by making or breaking connections among the gates
Programmable Array Block Diagram for Sum of Products Form
Inputs
Dense array of
AND gates
Product
terms
Dense array of
OR gates
Outputs

## Slide 14
PLD as a Black Box
Logic gates
and
programmable
switches
Inputs
(logic variables)
Outputs
(logic functions)

## Slide 15: Basic Programmable Logic Organizations
Depending on which of the AND/OR logic arrays is programmable, we have three basic organizations
AND ARRAY
PROG.
FIXED
PROG.
OR ARRAY
FIXED
PROG.
PROG.
ORGANIZATION
PAL
PROM
PLA

## Slide 16: Programming by blowing fuses.
(a) Before programming. (b) After programming.

## Slide 17: AND - PLD Notation

## Slide 18: OR - PLD Notation

## Slide 19
Memory and Programmable Logic

## Slide 20: Memory
Random Access Memory (RAM)
  Contrary to Serial Access Memory (e.g. Tape)
  Static Random Access Memory (SRAM)
    Data stored so long as Vdd is applied
    6-transistors per cell
    Faster
    Differential
  Dynamic Random Access Memory (DRAM)
    Require periodic refresh
    Smaller (can be implemented with 1 or 3 transistor)
    Slower
    Single-Ended
  Can be read and written
  Typically, addressable at byte granularity
Read-Only Memory (ROM)

## Slide 21: ROM Types
Mask programmable ROM
  fuses programmed during manufacture
Programmable ROM (PROM)
  0’s programmed by blowing fuses or “burning”
Erasable PROM (EPROM)
  programming erased by UV light
Electrically erasable PROM (EEPROM)
  programming erased via control signals

## Slide 22: Block Diagram of Memory
Example: 2MB memory, byte-addressable
  N = 8 (because of byte-addressability)
  K = 21 (1 word = 8-bit)
2k words
N-bit per word
Memory Unit
N-bit Data Input
(for Write)
N-bit Data Output
(for Read)
K-bit address lines
Read/Write
Chip Enable
N
N
K

## Slide 23: Memory Description
Capacity of a memory is described as
  # addresses x Word size
  Examples:
Memory | # of addr | # of data lines | # of addr lines | # of total bytes
1M x 8 | 1,048,576 | 8 | 20 | 1 MB
2M x 4 | 2,097,152 | 4 | 21 | 1 MB
1K x 4 | 1024 | 4 | 10 | 512 B
4M x 32 | 4,194,304 | 32 | 22 | 16 MB
16K x 64 | 16,384 | 64 | 14 | 128 KB

## Slide 24: How to Address Memory
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
0
1
2
3
D7
D6
D5
D4
D3
D2
D1
D0
4x8 Memory
2-to-4
Decoder
A0
A1
CS
Chip
Select

## Slide 25: How to Address Memory
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
0
1
2
3
D7
D6
D5
D4
D3
D2
D1
D0
4x8 Memory
2-to-4
Decoder
A0=1
A1=0
Access address = 0x1
CS
Chip
Select=1

## Slide 26: Use 2 Decoders
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
0
1
2
3
8x4 Memory
2-to-4
Decoder
Row
Decoder
A1
A2
1-to-2 Decoder Column Decoder
D0
D1
D2
D3
Tristate
Buffer
(read)
0
1
A0
CS
Chip
Select
CS

## Slide 27: Tristate Buffer
Similar to Transmission Gate
Could amplify signal (in contrast to a TG)
Typically used for signal traveling, e.g. bus
Input
Output
En
Input
Output
En

## Slide 28: Bi-directional Bus using Tri-state Buffer
Direction
(control data flow for read/write)
A
B
Input/Output

## Slide 29: Read/Write Memory
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
0
1
2
3
8x4 Memory
2-to-4
Row
Decoder
A1
A2
1-to-2 Column Decoder
D0
D1
D2
D3
0
1
A0
CS
Chip
Select = 0
CS
Rd/Wr = 0

## Slide 30: Read/Write Memory
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
0
1
2
3
8x4 Memory
2-to-4
Row
Decoder
A1
A2
1-to-2 Column Decoder
D0
D1
D2
D3
0
1
A0
CS
Chip
Select = 1
CS
Rd/Wr = 1

## Slide 31: Building Memory in Hierarchy
Design a 1Mx8 using 1Mx4 memory chips
D3
D2
D1
D0
A19
A18
A17
A0
1Mx4
R/W
CS
D7
D6
D5
D4
A19
A18
1Mx4
R/W
CS
A17
A0
CS

## Slide 32: Building Memory in Hierarchy
Design a 2Mx4 using 1Mx4 memory chips
A19
A18
A17
A0
1Mx4
R/W
CS
A19
A18
A17
A0
1Mx4
R/W
CS
A20
1-to-2
Decoder
CS
1
0
D3
D2
D1
D0
Note that 1-to-2
decoder is the wire
itself (or use
an inverter)

## Slide 33: Building Memory in Hierarchy
Design a 2Mx8 using 1Mx4 memory chips
A19
A18
A17
A0
1Mx4
CS
R/W
A19
A18
A17
A0
1Mx4
CS
R/W
A19
A18
A17
A0
1Mx4
CS
R/W
A19
A18
A17
A0
1Mx4
CS
R/W
D7
D6
D5
D4
D3
D2
D1
D0
A19
A18
A17
A0
A20
1-to-2
Decoder
CS
1
0

## Slide 34: Read Only Memory (ROM)
“Permanent” binary information is stored
Non-volatile memory
  Power off does not erase information stored
2k words
N-bit per word
ROM
N-bit Data Output
K-bit address lines
N
K

## Slide 35: Programming the 32x8 ROM
A4 | A3 | A2 | A1 | A0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
… | … | … | … | … | … | … | … | … | … | … | … | …
1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1
0
1
2
29
30
31
D7
D6
D5
D4
D3
D2
D1
D0
A4
A3
A2
A1
A0
5-to-32
Decoder

## Slide 36: Example: Lookup Table
Design a square lookup table for F(X) = X2 using ROM
X | F(X)=X2
0 | 0
1 | 1
2 | 4
3 | 9
4 | 16
5 | 25
6 | 36
7 | 49
X | F(X)=X2
000 | 000000
001 | 000001
010 | 000100
011 | 001001
100 | 010000
101 | 011001
110 | 100100
111 | 110001

## Slide 37: Square Lookup Table using ROM
X | F(X)=X2
000 | 000000
001 | 000001
010 | 000100
011 | 001001
100 | 010000
101 | 011001
110 | 100100
111 | 110001
0
1
2
3
F5
F4
F3
F2
F1
F0
X2
X1
X0
3-to-8
Decoder
4
5
6
7

## Slide 38: Square Lookup Table using ROM
X | F(X)=X2
000 | 000000
001 | 000001
010 | 000100
011 | 001001
100 | 010000
101 | 011001
110 | 100100
111 | 110001
0
1
2
3
F5
F4
F3
F2
F1
F0
X2
X1
X0
3-to-8
Decoder
4
5
6
7

## Slide 39: Square Lookup Table using ROM
X | F(X)=X2
000 | 000000
001 | 000001
010 | 000100
011 | 001001
100 | 010000
101 | 011001
110 | 100100
111 | 110001
= X0
Not Used
0
1
2
3
F5
F4
F3
F2
F1
F0
X2
X1
X0
3-to-8
Decoder
4
5
6
7

## Slide 40: Square Lookup Table using ROM
X | F(X)=X2
000 | 000000
001 | 000001
010 | 000100
011 | 001001
100 | 010000
101 | 011001
110 | 100100
111 | 110001
0
1
2
3
F5
F4
F3
F2
F0
X2
X1
X0
3-to-8
Decoder
4
5
6
7
F1

## Slide 41: PROM Notation

## Slide 42: Using a PROM for logic design
(a) Truth table. (b) PROM realization.

## Slide 43
Programmable Array Logic (PAL)
  Also used to implement circuits in SOP form
  The connections in the AND plane are programmable
  The connections in the OR plane are NOT programmable
f
1
AND plane
OR plane
Input buffers
inverters
and
P
1
P
k
f
m
x
1
x
2
x
n
x
1
x
1
x
n
x
n
fixed connections

## Slide 44
Example Schematic of a PAL
f
1
P
1
P
2
f
2
x
1
x
2
x
3
AND plane
P
3
P
4
f1 = x1x2x3'+x1'x2x3
f2 = x1'x2'+x1x2x3

## Slide 45
A simple four-input, three-output PAL device.

## Slide 46: PAL Logic Implementation
Programmed PAL:
4 product terms per each OR gate
Minimized Functions:
W = A + B D + B C
X = B C
Y = B + C
Z = A B C D + B C D + A D + B C D
A B C D
A B C D
A
BD
BC
0
0
0
0
B
C
0
0
BC
BCD
AD
BCD
W X Y Z

## Slide 47: PAL Logic Implementation
Design Example: BCD to Gray Code Converter
Truth Table
K-maps
Minimized Functions:
A
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
B
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
C
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
D
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
W
0
0
0
0
0
1
1
1
1
1
X
X
X
X
X
X
X
0
0
0
0
1
1
0
0
0
0
X
X
X
X
X
X
Y
0
0
1
1
1
1
1
1
0
0
X
X
X
X
X
X
Z
0
1
1
0
0
0
0
1
1
0
X
X
X
X
X
X
AB
CD
00
01
11
10
00
01
11
10
D
B
C
A
0
0
X
1
0
1
X
1
0
1
X
X
0
1
X
X
K-map for
W
AB
CD
00
01
11
10
00
01
11
10
D
B
C
A
0
1
X
0
0
1
X
0
0
0
X
X
0
0
X
X
K-map for
X
AB
CD
00
01
11
10
00
01
11
10
D
B
C
A
0
1
X
0
0
1
X
0
1
1
X
X
1
1
X
X
K-map for
Y
AB
CD
00
01
11
10
00
01
11
10
D
B
C
A
0
0
X
1
1
0
X
0
0
1
X
X
1
0
X
X
K-map for
Z
W = A + B D + B C
X = B C
Y = B + C
Z = A B C D + B C D + A D + B C D

## Slide 48: PAL Device Design Example
A
B
IO1
IO2
IO1
IO1
B
B
A
A
D
D
C
C
Not programmed

## Slide 49
An example of using a PAL device to realize two
Boolean functions. (a) Karnaugh maps. (b) Realization.

## Slide 50: PAL16V8 OLMC Configuration Modes
Simple mode (combinational output)
combinational output
combinational output with feedback
dedicated input
Complex mode
combinational output, with feedback
combinational input from another OLMC Registered mode: active (low, high): Q’ is feedback as input (no dedicated input)

## Slide 51
Programmable Logic Array (PLA)
  Use to implement circuits in SOP form
  The connections in the AND plane are programmable
  The connections in the OR plane are programmable
f
1
AND plane
OR plane
Input buffers
inverters
and
P
1
P
k
f
m
x
1
x
2
x
n
x
1
x
1
x
n
x
n

## Slide 52
Customary Schematic of a PLA
f1 = x1x2+x1x3'+x1'x2'x3
f2 = x1x2+x1'x2'x3+x1x3
f
1
P
1
P
2
f
2
x
1
x
2
x
3
OR plane
AND plane
P
3
P
4
x marks the connections left in place after programming

## Slide 53
Limitations of PLAs
  PLAs come in various sizes
    Typical size is 16 inputs, 32 product terms, 8 outputs
      Each AND gate has large fan-in  this limits the number of inputs that can be provided in a PLA
      16 inputs  316 = possible input combinations; only 32 permitted (since 32 AND gates) in a typical PLA
      32 AND terms permitted  large fan-in for OR gates as well
        This makes PLAs slower and slightly more expensive than some alternatives to be discussed shortly
      8 outputs  could have shared minterms, but not required

## Slide 54: PLA Logic Implementation
Example:
Equations
Personality Matrix
Key to Success: Shared Product Terms
1 = asserted in term
0 = negated in term
- = does not participate
1 = term connected to output
0 = no connection to output
Input Side:
Output Side:
Reuse
of
t
erms
F
1
1
0
1
0
0
Outputs
Inputs
Product
t
erm
A
1
-
1
-
1
B
1
0
-
0
-
C
-
1
0
0
-
F
0
0
0
0
1
1
F
2
1
0
0
1
0
F
3
0
1
0
0
1
A B
B C
A C
B C
A
F0 = A + B C
F1 = A C + A B
F2 = B C + A B
F3 = B C + A

## Slide 55: PLA Logic Implementation
Example Continued - Unprogrammed device
All possible connections are available
before programming
A
B
C
F0
F1
F2
F3

## Slide 56: PLA Logic Implementation
Example Continued -
Programmed part
Unwanted connections are "blown"
Note: some array structures
work by making connections
rather than breaking them
A
B
C
F0
F1
F2
F3
AB
BC
AC
BC
A

## Slide 57: PLA Logic Implementation
Alternative representation
Short-hand notation
so we don't have to
draw all the wires!
X at junction indicates
a connection
Notation for implementing
F0 = A B + A B
F1 = C D + C D
A B C D
AB+AB
CD+CD
AB
CD
CD
AB
Unprogrammed device
Programmed device

## Slide 58: PLA Logic Implementation
Design Example
F1 = A B C
F2 = A + B + C
F3 = A B C
F4 = A + B + C
F5 = A  B  C
F6 = A  B  C
Multiple functions of A, B, C
ABC
A
B
C
A
B
C
ABC
ABC
ABC
ABC
ABC
ABC
ABC
F1
F2
F3
F4
F5
F6
A
B
C

## Slide 59: PLA Logic Implementation
Another Example: Magnitude Comparator
A
K-map for
EQ
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
AB
CD
00
01
11
10
00
01
11
10
D
B
C
AB
CD
00
01
11
10
00
01
11
10
D
B
C
A
0
1
1
1
0
0
1
1
0
0
0
0
0
0
1
0
K-map for
GT
AB
CD
00
01
11
10
00
01
11
10
D
B
C
A
0
0
0
0
1
0
0
0
1
1
0
1
1
1
0
0
K-map for
L
T
0
1
1
1
1
0
1
1
1
1
0
1
1
1
1
0
AB
CD
00
01
11
10
00
01
11
10
D
B
C
K-map for
NE
A
EQ
NE
LT
GT
ABCD
ABCD
ABCD
ABCD
AC
AC
BD
BD
ABD
BCD
ABC
BCD
A B C D

## Slide 60: Programmable Logic Array (PLA)
C
B
A
C
C
B
B
A
A
F2
Programmable
AND Plane
Programmable
OR Plane

## Slide 61: Example using PLA
C
B
A
C
C
B
B
A
A
AB
AC
BC
A B C
F2
F1

## Slide 62
Comparing PALs and PLAs
  PALs have the same limitations as PLAs (small number of allowed AND terms) plus they have a fixed OR plane  less flexibility than PLAs
  PALs are simpler to manufacture, cheaper, and faster (better performance)
  PALs also often have extra circuitry connected to the output of each OR gate
    The OR gate plus this circuitry is called a macrocell

## Slide 63: FPGA AND CPLD
FPGA - Field-Programmable Gate Array.
CPLD - Complex Programmable Logic Device
FPGA and CPLD is an advanced PLD.
Support thousands of gate where as PLD only support hundreds of gates.

## Slide 64: CPLD and FPGA]
Complex Programmable Logic Device (CPLD)
  Multiple PLDs (e.g. PALs, PLAs) with programmable interconnection structure
  Pioneered by Altera
Field-Programmable Gate Array (FPGA)
  High logic capacity with large distributed interconnection structure
    Logic capacity  number of 2-input NAND gates
  Offers more narrow logic resources
    CPLD offers logic resources with a wide number of inputs (AND planes)
  Offer a higher ratio of Flip-flops to logic resources than CPLD
HCPLD (High Capacity PLD) is often used to refer to both CPLD and FPGA

## Slide 65: Programmable Logic Devices: CPLD vs FPGA
Complex Programmable Logic Device (CPLD): see (a) below
  Most of today’s CPLD’s are simply a collection of PLD’s on a chip interconnected by programmable interconnect (wiring)
Field Programmable Gate Array (FPGA): see (b) below
  FPGA’s are comprised of basic logic blocks interconnected by X and Y wiring channels

## Slide 66: CPLD
Complexity of CPLD is between FPGA and PLD.
CPLD featured in common PLD:-
  Non-volatile configuration memory – does not need an external configuration PROM.
  Routing constraints. Not for large and deeply layered logic.
CPLD featured in common FPGA:-
  Large number of gates available.
  Can include complicated feedback path.
CPLD application:-
  Address coding
  High performance control logic
  Complex finite state machines

## Slide 67: Complex Programmable Logic Devices
Complex PLDs typically combine PAL combinational logic with FFs
  Organized into logic blocks
  Fixed OR array size
  Combinational or registered output
  Some pins are inputs only
Usually enough logic for simple counters, state machines, decoders, etc.

## Slide 68: CPLD structure
PLD
PLD
PLD
PLD
PLD
PLD
PLD
PLD
Logic block
Interconnects
I/O block

## Slide 69: A General CPLD structure
A collection of PLDs on a single chip with
Programmble interconnects

## Slide 70: CPLD architecture
LAB – Logic Array Block / uses PALs
PIA – Programmable Interconnect Array

## Slide 71
Programming a CPLD
  CPLDs have many pins – large ones have > 200
    Removal of CPLD from a PCB is difficult without breaking the pins
    Use ISP (in system programming) to program the CPLD
    JTAG (Joint Test Action Group) port used to connect the CPLD to a computer

## Slide 72
Example CPLD
  Use a CPLD to implement the function
    f = x1x3x6' + x1x4x5x6' + x2x3x7 + x2x4x5x7

## Slide 73: FPGA?
Before the advent of programmable logic, custom logic circuits were built at the board level using standard components, or at the gate level in expensive application-specific (custom) integrated circuits.
FPGA is an integrated circuit that contains many (64 to over 10,000) identical logic cells that can be viewed as standard components. Each logic cell can independently take on any one of a limited set of personalities.
Individual cells are interconnected by a matrix of wires and programmable switches. A user's design is implemented by specifying the simple logic function for each cell and selectively closing the switches in the interconnect matrix.
Array of logic cells and interconnect form a fabric of basic building blocks for logic circuits. Complex designs are created by combining these basic blocks to create the desired circuit

## Slide 74: Field Programmable Gate Arrays (FPGAs)
FPGAs have much more logic than CPLDs
  2K to >10M equivalent gates
  Requires different architecture
  FPGAs can be RAM-based or Flash-based
    RAM FPGAs must be programmed at power-on
      External memory needed for programming data
      May be dynamically reconfigured
    Flash FPGAs store program data in non-volatile memory
      Reprogramming is more difficult
      Holds configuration when power is off

## Slide 75: FPGA Structure
Typical organization in 2-D array
  Configurable logic blocks (CLBs) contain functional logic (could be similar to PAL22V10)
    Combinational functions plus FFs
    Complexity varies by device
  CLB interconnect is either local or long line
    CLBs have connections to local neighbors
    Horizontal and vertical channels used for long distance
    Channel intersections have switch matrix
  IOBs (I/O logic Blocks) connect to pins
    Usually have some additional Combinational Logic./FF in block

## Slide 76: Field-Programmable Gate Arrays structure
Logic blocks
  To implement combinational and sequential logic
Interconnect
  Wires to connect inputs and outputs to logic blocks
I/O blocks
  Special logic blocks at periphery of device for external connections

## Slide 77: FPGA architecture

## Slide 78: FPGA Structure
Logic block
I/O block
Interconnects

## Slide 79: what does 'Field Programmable' mean?
Field Programmable means that the FPGA's function is defined by a user's program rather than by the manufacturer of the device.
A typical integrated circuit performs a particular function defined at the time of manufacture. In contrast, the FPGA's function is defined by a program written by someone other than the device manufacturer.
Depending on the particular device, the program is either 'burned' in permanently or semi-permanently as part of a board assembly process, or is loaded from an external memory each time the device is powered up.
This user programmability gives the user access to complex integrated designs without the high engineering costs associated with application specific integrated circuits.

## Slide 80: How are FPGA programs created?
Individually defining the many switch connections and cell logic functions would be a daunting task.
This task is handled by special software. The software translates a user's schematic diagrams or textual hardware description language code then places and routes the translated design.
Most of the software packages have hooks to allow the user to influence implementation, placement and routing to obtain better performance and utilization of the device.
Libraries of more complex function macros (eg. adders) further simplify the design process by providing common circuits that are already optimized for speed or area.

## Slide 81
FPGA
  SPLDs and CPLDs are relatively small and useful for simple logic devices
    Up to about 20000 gates
  Field Programmable Gate Arrays (FPGA) can handle larger circuits
    No AND/OR planes
    Provide logic blocks, I/O blocks, and interconnection wires and switches
    Logic blocks provide functionality
    Interconnection switches allow logic blocks to be connected to each other and to the I/O pins

## Slide 82
LUTs
  Logic blocks are implemented using a lookup table (LUT)
    Small number of inputs, one output
    Contains storage cells that can be loaded with the desired values
    A 2 input LUT uses 3 MUXes to implement any desired function of 2 variables
      Shannon's expansion at work!
f
0/1
0/1
0/1
0/1
x
1
x
2

## Slide 83
Programming an FPGA
  ISP method is used
  LUTs contain volatile storage cells
    None of the other PLD technologies are volatile
    FPGA storage cells are loaded via a PROM when power is first applied
  The UP2 Education Board by Altera contains a JTAG port, a MAX 7000 CPLD, and a FLEX 10K FPGA
    The MAX 7000 CPLD chip is EPM7128SLC84-7
    EPM7  MAX 7000 family; 128 macrocells; LC84  84 pin PLCC package; 7  speed grade

## Slide 84: FPGA
FPGA applications:-
  DSP
  Software-defined radio
  Aerospace
  Defense system
  ASIC Prototyping
  Medical Imaging
  Computer vision
  Speech Recognition
  Cryptography
  Bioinformatic
  And others.

## Slide 85: Application Specific Chips (ASIC)
Custom Chips
  PLDs are limited by number of programmable switches
    Consume space
    Reduce speed
  Custom chips are created from scratch
    Expensive  used when high speed is required, volume sales are expected, and chip size is small but with high density of gates
    ASICs (Application Specific Integrated Circuits) are custom chips that use a standard cell layout to reduce design costs

## Slide 86: Standard Cells
Standard Cells
  Rows of logic gates can be connected by wires in the routing channels
    Designers (via CAD tools) select prefab gates from a library and place them in rows
    Interconnections are made by wires in routing channels
      Multiple layers may be used to avoid short circuiting
      A hard-wired connection between layers is called a via

## Slide 87: Standard Cells

## Slide 88
Example: Standard Cells
  f1 = x1x2 + x1'x2'x3 + x1x3'
  f2 = x1x2 + x1'x2'x3 + x1x3

## Slide 89: Sea of Gates Gate Array
Sea of Gates Gate Array
  A Sea of Gates gate array is just like a standard cell except all gates are of the same type
    Interconnections are run in channels and use multiple layers
    Cheaper to manufacture due to regularity

## Slide 90: Sea of Gates Gate Array

## Slide 91
Example: Sea of Gates
  f1 = x2x3' + x1x3